## Slide 1
Calibration framework: growth parameters from the final 3D scan
θ → growth-metric forward simulation → material-frame shape score vs. scan → GP surrogate + batch qLogEI → next θ
1
Parameters & search space
Four per-pass growth parameters of the bilayer shell model (top/bottom growth, top/bottom orthotropy):
Optimized in the unit cube x ∈ [0,1]⁴: logarithmic in growth, linear in orthotropy.
Bounds: g_top ∈ [5×10⁻⁵, 10⁻²], g_bot ∈ [10⁻⁵, 10⁻³], o_top, o_bot ∈ [−1, 1].
Four per-pass growth parameters of the bilayer shell model (top/bottom growth, top/bottom orthotropy):
θ = (g_top, g_bot, o_top, o_bot)
Optimized in the unit cube x ∈ [0,1]⁴: logarithmic in growth, linear in orthotropy.
x_g = (ln g − ln g_min)/(ln g_max − ln g_min), x_o = (o+1)/2
Bounds: g_top ∈ [5×10⁻⁵, 10⁻²], g_bot ∈ [10⁻⁵, 10⁻³], o_top, o_bot ∈ [−1, 1].
2
Forward model: zigzag toolpath → bilayer shell
Run6: 68-strip zigzag pass repeated 29×. Each hit on face f grows the target metrics, with hit-count (Voce) decay:
After all passes, solve elastic equilibrium once (native hybrid solver, ‖∇E‖ ≤ 5×10⁻¹⁴):
Run6: 68-strip zigzag pass repeated 29×. Each hit on face f grows the target metrics, with hit-count (Voce) decay:
q_n = exp(−βn), β = ln 1.25; g_{1,2}^ℓ = q_n g_ℓ (1 ± o_ℓ)
ā_ℓ ← Tᵀ ā_ℓ T, T = D_m⁻¹ R_φ diag(1+g₁, 1+g₂) R_φᵀ D_m
After all passes, solve elastic equilibrium once (native hybrid solver, ‖∇E‖ ≤ 5×10⁻¹⁴):
x*(θ) = argmin_x E_bilayer(x; ā_top, ā_bot)
3
Shape score against the 3D scan
Rigid frame set by the material reference, not fitted to the scan: Kabsch rotation of deformed onto flat reference vertices; area-weighted centroid removed; scan centered.
Symmetric RMS surface discrepancy (scan → simulated surface, and area-weighted simulated vertices → scan):
yᵢ: N scan points (2 mm grid); S_θ: simulated surface; pⱼ: simulated vertices; wⱼ = Aⱼ / Σₖ Aₖ (reference dual areas).
Rigid frame set by the material reference, not fitted to the scan: Kabsch rotation of deformed onto flat reference vertices; area-weighted centroid removed; scan centered.
R = argmin_{R∈SO(3)} Σ_j ‖R(p_j − p̄) − (X_j − X̄)‖²
Symmetric RMS surface discrepancy (scan → simulated surface, and area-weighted simulated vertices → scan):
L_sym = sqrt(½[(1/N)Σ d(y_i,S_θ)² + Σ w_j min_i ‖p_j − y_i‖²])
yᵢ: N scan points (2 mm grid); S_θ: simulated surface; pⱼ: simulated vertices; wⱼ = Aⱼ / Σₖ Aₖ (reference dual areas).
4
Batch Bayesian optimization (BoTorch)
Gaussian-process surrogate of the log-misfit with a Matérn-5/2 ARD kernel:
Each wave proposes q = 4 parallel solves by maximizing batch log expected improvement (qLogEI):
Failed/timed-out solves are excluded from the GP; proposals keep ‖Δx‖ ≥ 0.08; stop at the evaluation budget or 6 consecutive failures.
Gaussian-process surrogate of the log-misfit with a Matérn-5/2 ARD kernel:
f(x) = −ln L_sym(x) ~ GP(μ, k)
k = σ²(1 + √5 r + 5r²/3) exp(−√5 r)
Each wave proposes q = 4 parallel solves by maximizing batch log expected improvement (qLogEI):
{x_1..x_4} = argmax ln E[max_j (f(x_j) − f*)_+]
Failed/timed-out solves are excluded from the GP; proposals keep ‖Δx‖ ≥ 0.08; stop at the evaluation budget or 6 consecutive failures.
Implementation: calibration/ewcal (runner.py, material_frame.py, geometry.py, batch_bayes.py); shell solver src/simulations/Sim_Bilayer_Growth.cpp. Run6 continuation (in progress, 14 Oct 2026): best L_sym = 1.18 mm (Attempt 187).